## Slide 1: Tacheometry surveying
It means the fast measurment of the distances in both types ( horizantal & vertical ) . It is a type of optical distance measurment.

## Slide 2: Tacheometry surveying
Advantages of tacheometry surveying :
1- Fast measurment of distances.
2- More accurate measurment than the ordinary once & its accuracy from 1\500 ---1\10000 .
3- It can be used in bad conditions of measuring .

## Slide 4: Tacheometry surveying
Types of instruments were used :
1- Level & staff.
2- Theodolite & staff.
3- Alidade with plane table & staff .
4- Reduced tacheometry & staff .
5- Subtense bar with theodolite .

## Slide 5: Reduction tacheometry
In this type neednt read vertical angles only reading reduction staff as following :
Zero curve
Height Curve
Distance Curve
(0.1, 0.2 ,---)+, -

## Slide 6: Reduction tacheometry
V.D = F * K * S 2
H.D = K * S1
F : middle curve factor.
K : multiplier constant = 100
S2= middle curve reading – zero curve reading
S1= distance curve reading – zero curve reading
V.D : vertical distance
H.D: horizontal distance

## Slide 7: Reduction tacheometry
When we calculate the differnce in elevation between two stations take zero curve reading as RR
Always = 1 m in leica type
Or 1.4 m in dalta type

## Slide 8: Test :
What are the differentes between the mechnical & reduction theodolite ?

## Slide 9: Thank you